SLVM instruction set

Mnemonic	Opcode	Parameters	Stack	Description
nop	00			No operation.
const4	0a	value [4 bytes]	→ value	Pushes a 4 byte value onto the stack.
laddr	10	local address [int16]	→ value	Pushes an address of a local variable into the stack.
load4	11		address → value	Pushes a 4 byte value from address onto the stack.
lload4	12	local address [int16]	→ value	Pushes a 4 byte value from local address onto the stack.
store4	13		address, value →	Stores a 4 byte value from the stack at address.
lstore4	14	local address [int16]	value →	Stores a 4 byte value from the stack at local address.
addi	30		left, right → result	Adds two int numbers.
addf	31		left, right → result	Adds two float numbers.
subi	38		left, right → result	Subtracts two int numbers.
subf	39		left, right → result	Subtracts two float numbers.
muli	40		left, right → result	Multiplies two int numbers.
mulf	41		left, right → result	Multiplies two float numbers.
divi	48		left, right → result	Divides two int numbers.
divf	49		left, right → result	Divides two float numbers.
modi	50		left, right → result	Computes modulo of two int numbers.
modf	51		left, right → result	Computes modulo of two float numbers.
negi	58		value → value	Negates the value on the stack.
negf	59		value → value	Negates the value on the stack.
andi	60		value → value	Computes bitwise and on two int numbers.
ori	62		value → value	Computes bitwise or on two int numbers.
xori	64		value → value	Computes bitwise xor on two int numbers.
noti	66		value → value	Computes bitwise not on an int number.
i2f	70		value → result	Converts an int into a float.
f2i	71		value → result	Converts a float into an int.
jump	80		address →	Jumps to a given address.
call	81		address → return address	Jumps to a subroutine and stores the return address of the stack.
enter	82	size [uint16]	→ 4 + size bytes	Allocates stack space for local variables.
leave	83			Releases stack space.
ret	84		return address →	Jumps to a given address (returns from a subroutine).
pop	85	size [uint8]	size bytes →	Pops size bytes from the stack.
cjump	86		address, cond →	Jumps to a given address if cond ≠ 0.
lti	90		left, right → result	Compares two int numbers. Returns 1 if left < right. 0, otherwise.
ltf	91		left, right → result	Compares two float numbers. Returns 1 if left < right. 0, otherwise.
lei	98		left, right → result	Compares two int numbers. Returns 1 if left ≤ right. 0, otherwise.
lef	99		left, right → result	Compares two float numbers. Returns 1 if left ≤ right. 0, otherwise.
gti	a0		left, right → result	Compares two int numbers. Returns 1 if left > right. 0, otherwise.
gtf	a1		left, right → result	Compares two float numbers. Returns 1 if left > right. 0, otherwise.
gei	a8		left, right → result	Compares two int numbers. Returns 1 if left ≥ right. 0, otherwise.
gef	a9		left, right → result	Compares two float numbers. Returns 1 if left ≥ right. 0, otherwise.
eqi	b0		left, right → result	Compares two int numbers. Returns 1 if left = right. 0, otherwise.
eqf	b1		left, right → result	Compares two float numbers. Returns 1 if left = right. 0, otherwise.
neqi	b8		left, right → result	Compares two int numbers. Returns 1 if left ≠ right. 0, otherwise.
neqf	b9		left, right → result	Compares two float numbers. Returns 1 if left ≠ right. 0, otherwise.
inpi	fc	local address [int16]		Reads an int from the console into given address. / Warning! For testing purposes only!
outi	fd	local address [int16]		Prints an int on the console. / Warning! For testing purposesonl